## Slide 1
SiteShield.ai
Real-Time Data Ingestion Architecture
From Raw Hardware to AI-CRV Risk Intelligence
L1 Hardware Sources
L2 Protocol Adapters
L3 Normalization & QC
L4 Message Broker
L5 Consumers
L6 Dashboard
Target Use: Technical Presentation Diagram Style: Professional technical architecture diagram Recommended Tools: Eraser.io, Lucidchart, Miro, or any AI diagramming tool

## Slide 2
Overview
Data flow: hardware → adapters → normalization → broker → AI-CRV → dashboard
ARCHITECTURE — TOP-TO-BOTTOM FLOW
L1
Physical Data Sources
Sensors, SCADA, cameras, detectors, telematics, external feeds
L2
Protocol Adapters
One per protocol family — translates raw to JSON
L3
Normalization & QC
Schema mapping, units, UTC time, confidence, anomaly pre-filter
L4
Message Broker
MQTT (edge) / Kafka (cloud) — pub/sub decoupling
L5
Consumers
AI-CRV engine, modules, alerts, audit, AI safety adviser
L6
Dashboard
React web app — composite score, modules, alerts, map

## Slide 3
Industrial & Machine Protocols (Boxes A, B, & D)
These are the rugged, "old-school" languages used by sensors and heavy machinery in the field.
4-20mA: An analog electrical standard where the amount of current (milliamps) tells the system a value, like how high the pressure is.
HART: A way for "smart" sensors to send digital data over the same wires used for the 4-20mA signal.
Modbus (RTU & TCP): One of the most common languages in the world for industrial electronics. RTU usually travels over simple wires, while TCP travels over a standard computer network.
OPC-UA: A modern, secure way for different types of industrial "brains" (like PLCs) to talk to each other, regardless of who manufactured them.
DNP3: Mainly used in the power and water industries to make sure data is delivered reliably, even if the connection is slow or patchy.
RS-485: A technical standard for the physical wires that carry serial data over long distances in noisy industrial environments.
Camera & Video Standards (Box C)
These protocols ensure the video feeds from the rig floor or perimeter can be viewed and recorded properly.
RTSP (Real Time Streaming Protocol): The "remote control" for a video stream; it handles the play, pause, and setup of the connection.
H.264: A compression method that shrinks high-definition video files so they can be sent over the internet without using too much bandwidth.
ONVIF: A global standard that allows a camera from Brand A to work seamlessly with software from Brand B.
Modern IoT & Web Protocols (Boxes D, E, & F)
These are "internet-native" languages used by modern software, mobile devices, and global data feeds.
MQTT (Message Queuing Telemetry Transport): A very "lightweight" language perfect for small devices (like sensors) that need to send updates frequently without using much power.
REST / REST API: The standard way most apps on your phone or computer talk to servers. It’s like a menu: the system asks for a specific "dish" of data, and the server provides it.
JSON (JavaScript Object Notation): A simple text format for storing and transporting data. It looks like a list of labels and values (e.g., "Temperature": "25"), making it easy for both humans and computers to read.
WebSocket: Unlike a standard request, a WebSocket keeps a "phone line" open all the time so the server can push new information to the platform the second it happens.
4G LTE: The high-speed cellular network used to transmit data from moving vehicles or remote sites back to the main system.
Layer 1 — Physical Data Sources
Six hardware source groups feeding the ingestion pipeline
[A] Sensors & Instruments
Gas detectors (H2S, LEL, O2)
Pressure & temperature transmitters
Flow meters
Vibration sensors
4-20mA / HART / Modbus RTU
[B] SCADA / DCS Systems
Wellhead control panels
Process control units
PLC outputs
OPC-UA / Modbus TCP / DNP3
[C] CCTV & Thermal Cameras
Fixed IP cameras (perimeter)
PTZ cameras (rig floor)
Thermal imaging units
RTSP / H.264 / ONVIF
[D] Detection Devices
Radiation monitors (NORM/radioactive)
Explosive trace detectors
Acoustic pig-passage detectors (BIRD)
Radar / LiDAR (drone detection)
Serial RS-485 / MQTT / Proprietary API
[E] Vehicle & Fleet Telematics
GPS trackers
In-cab driver monitoring cameras
CAN bus (speed, braking, seatbelt)
4G LTE / MQTT / REST API
[F] External Data Feeds
Weather APIs
AIS vessel tracking
Intel / security threat feeds
REST / WebSocket / JSON
Notes: Industrial & Machine Protocols (Boxes A, B, & D)
These are the rugged, "old-school" languages used by sensors and heavy machinery in the field.
4-20mA: An analog electrical standard where the amount of current (milliamps) tells the system a value, like how high the pressure is.
HART: A way for "smart" sensors to send digital data over the same wires used for the 4-20mA signal.
Modbus (RTU & TCP): One of the most common languages in the world for industrial electronics. RTU usually travels over simple wires, while TCP travels over a standard computer network.
OPC-UA: A modern, secure way for different types of industrial "brains" (like PLCs) to talk to each other, regardless of who manufactured them.
DNP3: Mainly used in the power and water industries to make sure data is delivered reliably, even if the connection is slow or patchy.
RS-485: A technical standard for the physical wires that carry serial data over long distances in noisy industrial environments.
Camera & Video Standards (Box C)
These protocols ensure the video feeds from the rig floor or perimeter can be viewed and recorded properly.
RTSP (Real Time Streaming Protocol): The "remote control" for a video stream; it handles the play, pause, and setup of the connection.
H.264: A compression method that shrinks high-definition video files so they can be sent over the internet without using too much bandwidth.
ONVIF: A global standard that allows a camera from Brand A to work seamlessly with software from Brand B.
Modern IoT & Web Protocols (Boxes D, E, & F)
These are "internet-native" languages used by modern software, mobile devices, and global data feeds.
MQTT (Message Queuing Telemetry Transport): A very "lightweight" language perfect for small devices (like sensors) that need to send updates frequently without using much power.
REST / REST API: The standard way most apps on your phone or computer talk to servers. It’s like a menu: the system asks for a specific "dish" of data, and the server provides it.
JSON (JavaScript Object Notation): A simple text format for storing and transporting data. It looks like a list of labels and values (e.g., "Temperature": "25"), making it easy for both humans and computers to read.
WebSocket: Unlike a standard request, a WebSocket keeps a "phone line" open all the time so the server can push new information to the platform the second it happens.
4G LTE: The high-speed cellular network used to transmit data from moving vehicles or remote sites back to the main system.

## Slide 4
Layer 2 — Protocol Adapters
One adapter per protocol family — translates raw data into a standard internal format
[A] Modbus / HART Adapter
→ Handles: analog sensors, instruments, PLCs → Outputs: normalized JSON telemetry object
[B] OPC-UA Adapter
→ Handles: SCADA, DCS, process control systems → Outputs: normalized JSON telemetry object
[C] RTSP / Video Adapter
→ Handles: IP cameras, thermal feeds → Outputs: frame objects with metadata + AI vision inference results
[D] MQTT Adapter
→ Handles: IoT sensors, detection devices, some fleet devices → Outputs: normalized JSON telemetry object
[E] REST / WebSocket Adapter
→ Handles: fleet telematics, external APIs, weather feeds → Outputs: normalized JSON telemetry object
DESIGN PRINCIPLE
One adapter per PROTOCOL — not per device. A single MQTT adapter handles all MQTT-compliant hardware.
STANDARD OUTPUT
Adapters output a normalized JSON telemetry object that flows into Layer 3 (Normalization Engine) regardless of source protocol.

## Slide 5
Layer 3 — Normalization & Quality Control
All adapter outputs feed into a single processing pipeline — the most important layer
Step 1 — Schema Mapping
All inputs mapped to Canonical Telemetry Object (CTO) | Fields: sourceId, moduleTag, timestamp (UTC), value, unit, quality, sensorStatus, rawProtocol
Step 2 — Unit Standardization
Pressure → PSI | Temperature → °C | Flow → m³/hr | Ensures uniform units regardless of sensor manufacturer
Step 3 — Timestamp Normalization
All timestamps converted to UTC ISO 8601 | Latency flagged if timestamp delta > threshold
Step 4 — Quality & Confidence Scoring
Each data point receives a confidence score (0.0–1.0) | Factors: signal strength / SNR, data freshness (staleness penalty), sensor health (fault flags), dropout detection
Step 5 — Anomaly Pre-Filter
Out-of-range values flagged before reaching AI engine | Does NOT discard — flags for AI-CRV handling
CANONICAL TELEMETRY OBJECT
{ sourceId: "GD-P03-H2S-001", moduleTag: "OPS_RISK", timestamp: "2026-05-05T14:32:11.204Z", value: 12.4, unit: "ppm", quality: 0.91, sensorStatus: "NORMAL", rawProtocol: "MODBUS_TCP" }

## Slide 6
Layer 4 — Message Broker / Event Bus
Pub/sub backbone — hardware and AI engine remain fully decoupled
MQTT Broker / Apache Kafka (scale-out)
DEMO / EDGE DEPLOYMENT
MQTT (lightweight)
Operates fully offline on edge hardware. No cloud dependency for core risk scoring.
ENTERPRISE / CLOUD DEPLOYMENT
Apache Kafka (high-throughput, replay)
Horizontal scale, durable storage, full event replay for compliance & forensic analysis.
PUB / SUB DECOUPLING
All downstream consumers subscribe — they never poll hardware directly. Hardware and AI engine are fully independent. Adapter failure does not crash the engine.

## Slide 7
Layer 5 — Consumers
Subscribers pulling from the broker — AI-CRV is the core engine
[A] AI-CRV INFERENCE ENGINE — CORE engine (Patent-Pending)
Confidence-weighted multi-model scoring Asymmetric override logic | Temporal smoothing (EMA) Outputs: Composite Risk Score (0–100), topDrivers, overrideLevel
[B] MODULE PROCESSORS (one block per active module)
Threat Detection (Drone/Perimeter)
Operational Risk (Pipeline Pigging)
Rig Floor Safety (RigShield)
Vehicle Safety
Radioactive Source Monitor
Explosive Device Detection
[C] ALERT ENGINE
Threshold evaluation • Escalation: INFO → WARNING → CRITICAL → EMERGENCY
[D] AUDIT & HISTORIAN
Immutable time-series log • Regulatory compliance record • Replay capability for incident investigation
[E] AI SAFETY ADVISER
Natural language risk explanation • Powered by: Google Gemini API (online) • Fallback: Local Ollama model (offline / edge)

## Slide 8
Layer 6 — SiteShield.ai Dashboard
Final output — operator-facing real-time interface
React Web Dashboard
Real-time Composite Risk Score
0–100 with override level
Module Tabs
drill-down per module
Alerts & Actions
operator response workflows
Map View
spatial situational awareness
Role-Based Views
Operator / Supervisor / Safety Officer

## Slide 9
Visual Design Instructions
Color scheme | Layout | Typography | Format
COLOR SCHEME
#080E1A
Background (dark navy)
#00C2FF
Layer labels (cyan accent)
#1A2A3A
Hardware blocks (dark grey)
#F6AD55
AI-CRV highlight (gold/amber)
#FFFFFF
Arrows (white / cyan)
#3D52A0
Indigo (light-mode label)
LAYOUT
Preferred orientation: top-to-bottom (vertical flow)
Layer labels on left margin as section dividers
Each layer separated by horizontal rule or background band
Arrows show data direction clearly
Group hardware sources with bounding box labeled “Field Layer”
Normalization: highlighted with accent border + subtle glow
Message Broker: full-width horizontal bar
AI-CRV Engine: distinct gold/amber highlight
TYPOGRAPHY + FORMAT
Layer titles: Bold, uppercase, 14-16pt Block labels: Bold, 12pt Sub-items: Regular, 10-11pt Protocol labels: Italic / monospace, smaller CTO example: Monospace (Courier, Fira Code) Format Target: 16:9 widescreen (1920×1080) or A3 landscape Legible when projected Export PNG or SVG for embedding

## Slide 10
Optional Callout Boxes
Add to the diagram if space permits
Demo Mode
Simulated data injected at Layer 3 output. Bypasses Layers 1-2. Engine behavior identical to production.
Patent-Pending
AI-CRV: Asymmetric confidence-weighted multi-criteria aggregation with temporal filtering and safety override logic.
Edge-Ready
Operates fully offline on edge hardware. No cloud dependency for core risk scoring.

## Slide 11
End-to-End Architecture
All six layers — top-to-bottom flow
L1 PHYSICAL DATA SOURCES
Sensors
SCADA/DCS
Cameras
Detectors
Telematics
Ext. Feeds
L2 PROTOCOL ADAPTERS
Modbus/HART
OPC-UA
RTSP/Video
MQTT
REST/WS
L3 NORMALIZATION & QUALITY CONTROL
Schema → Units → UTC → Confidence → Anomaly Pre-Filter
L4 MESSAGE BROKER (MQTT / Apache Kafka)
Pub/Sub Event Bus — full-width decoupling
L5 CONSUMERS
AI-CRV Engine ★
Modules ×6
Alerts
Audit/Historian
AI Adviser
L6 DASHBOARD
React Web App — Composite Score, Modules, Alerts, Map, Roles